Digital Design VHDL Project Report

Introduction

The aim of this project was to create a peak detector that when fed a series of hexadecimal data values the peak value was identified along with the proceeding and previous 3 values. This detector is run on a Xilinx X5 FPGA development
board and communications between the board and desktop computer is handled via the UART RS-232 protocol. Along with the main feature of peak detection, the system had to respond to certain input commands and produce results as requested. These features are detailed below.

Group

As group 17, our four person group consisted of Daryl White, Alexander Hamilton, Sylvia Betrosian and Andreas Michaelides. We met initially to discuss the project and split up into pairs to work on the Data Processor and Command Processor. Daryl White and Alexander Hamilton designed and built the Data Processor and Sylvia Betrosian and Andreas Michaelides designed and built the Command Processor.

Plan

A large part of this assignment was learning to break down large portions of the project into smaller tasks that could be allocated to each group member and the experience of coordinating work efforts so that each component integrated correctly once the final system was built.

Our group decided to meet every two weeks to discuss progress and problems and, before the interim deadline, test the interaction of the data processor and command processor.

Within each two person team a Gantt chart was drawn up to plan when each segment of the respective processor should be completed by.

Gantt Chart and key milestone dates.

The key milestones for this project were the interim assignment deadline (working code and report) on Friday 24th March and the final synthesised deadline on 28th April and the presentation date of

Data Processor

The first step in designing the data processor was to understand the functionality required then implement this in a state machine.

Below is the finite state machine diagram.

This was then converted to an ASM chart so the states could be created using simple conditionals in VHDL.

Below is the ASM Chart

To explain the data processor we have broken this section into architecture, signals and processes and gone into detail about our choices within each section.

Architecture

We decided to use a single architecture called ‘dataConsume’, we initially considered multiple architectures for modularity but felt that this would increase complexity and possible duplication of signals.

States

The follow states where used in our state machine

1) init – This is the initial state that waits for the ‘start’ signal to arrive from the command processor before moving on to ‘dataRequest’

2) dataRequest – Second state that is conditional upon a signal ‘dataArrived’ which signifies when data is being received from the data generator.

3)sendBytes – Third state checks for the end condition of all data being received from the data generator before moving onto the peak byte assignment.

4)assignPeak – Forth state that assigns the peak byte, three preceding bytes and three post bytes.

5)sendPeak – Fifth state, this is the final state that sends the results to the command processor and returns to the initial state.

Signals

curState, nextState: state_type; - Used for moving through the state machine

numWordsReg: BCD_ARRAY_TYPE(2 downto 0); -Stores ‘numWords’ in a register.

integerPosistion3,integerPosistion2,integerPosistion1, totalSum : integer; - Integers involved in ‘numWords’.

N: integer := 0; - Controls the allocation of the data into the array.

resetN: std_logic; - Resets ‘N’ back to zero when in ‘init’ state.

beginRequest, endRequest: std_logic; - Tell the processor to stop and start requesting data from the generator.

totalDataArray : CHAR_ARRAY_TYPE(0 to 999); Stores every byte received.

rollingPeakBin : signed(7 downto 0) := "10000001"; - Peak byte in binary.

peakIndex: integer; --Index of peak byte ## Just remember that maxIndex is BCD_ARRAY_TYPE ##

ctrl_2Delayed, ctrl_2Detection: std_logic; - Ctrl_2 detection signals.

resultsValid, byteReady: std_logic; - ByteReady is not used*

dataArrived: std_logic; - Check that data has started to be allocated into the global array.

conversionComplete: std_logic; - Check that ‘peakIndex’ has been converted into a BCD format.
Processes

Processes handling the state machine

state_reg: process(clk, reset) - This process returns the state machine to the initial state upon the reset signal going high and changes the current state to the next state on the clock edge.

state_order: process(clk,curState) – The main state machine process, this is responsible for executing conditionals in each state.

combinational_output:process(curState) – As we are using Moore architecture this process provides the outputs for the states.

 Processes handling numWords_BCD

register_numWords:process(start, clk) – This is just a simple register to store the value numWords_bcd on the rising clock edge. This is an easy way to avoid latches.
convert_numWords:process(numWordsReg, reset) – This is the process for converting each digit in numWords_bcd into a way that is readable for our machine. This is done by converting each of the bit vectors into unsigned bit arrays followed by integers.

summing_numWords:process(integerPosistion1, integerPosistion2, integerPosistion3) – each of the integers are then multiplied by their corresponding position (integerposition3 represents the hundreds and is therefore multiplied by 100) and summed together to produce the integer format of numWords_bcd which is saved as a signal in the form of ‘totalSum’.

Processes handling the handshaking protocol

request_data:process(CLK, reset, resetN) – This is the process responsible for requesting data from the data generator. The data generator prepares a new byte of data to send when there is a change in the output from the data processor. This is done by having ctrlOut being assigned the ‘switching’ variable whenever there is a rising clock edge and beginRequest is high. The value for switching is then inverted and a ‘switchCounter’ variable increases by 1. When the switchCounter is greater than the totalSum, ctrlOut will stop changing and hence data will stop being requested.

delay_ctrl_2:process(clk) – This process saves the value of what is currently ctrlIn into a register. This registered value is then compared below in the global_data_array process

Storing data processes

send_byte:process(totalDataArray,clk)

global_data_array: process(clk,beginRequest) –This process is responsible for saving the data coming into the data processor from the data generator. It first XOR’s the values of ctrl_2Delayed and ctrlIn to check if they are different. If they are different, this allows this process to detect a change in the value of ctrlIn which represents that the data from the generator is ready. The process then saves this data value into the Nth position in the global data array. N is then increased by 1 and the signal representing that the first byte of data has been saved, is asserted. The array will stop saving values into the array then the value of N is greater than the totalSum – 1 in which a signal will be asserted to represent the end of the assignment of data bytes.

detector actually starts comparing values

detector: process(clk,totalDataArray, reset, resetN)
peakIndex_to_BCD:process(peakIndex, clk, reset)

requested_results: process(reset, resultsValid)--the peak index will be in BCD format so not sure how correct this will be (Alex)

GitHub – We used git for our version control system and our code is available on github at https://github.com/darylw357/digital_design_group

We felt it was important do this as we could track each change made by our respective partner and reduced the chance of duplicated efforts or code breaking. It also allowed us to get the core functionality then improve upon that with experimental branches without risking our working project.

Command Processor

Group to add their report here.

Conclusion

This digital design project provided challenges in designing a complex system within the VHD language and working within unfamiliar groups to achieve a common goal. However we , as a group, felt that overall this project was successful in implementing the required specification of a hexadecimal data peak detector on Xilinx hardware.